## Slide 1: Control-Signal Crosstalk in Flip-Chip
Superconducting Quantum Processors
Sandoko Kosen (Chalmers University of Technology)
Packaged Flip-Chip Module
Chip Design & Fabrication by Chalmers
Flip-Chip Packaging by VTT
Sample Holder & PCB concept by Chalmers
Q72.00010
CHALMERS Team
Tahereh Abad
Anuj Aggarwal Janka Biznárová Liangyu Chen Miroslav Dobsicek
Jorge Fernández-Pendás Simon Pettersson Fors Göran Johansson Sandoko Kosen Christian Križan
Hang-Xi Li
Eleftherios Moschandreou
Andreas Nylander
Amr Osman Robert Rehammar Marcus Rommel
Anita Fadavi Roudsari
Daryoush Shiri
Tom Vethaak Christopher Warren Alexey Zadorozhko Anton Frisk Kockum Giovanna Tancredi Per Delsing
Jonas Bylander
VTT Team
Marco Caputo Leif Grönberg Kestutis Grigoras Joonas Govenius

## Slide 2: 1st generation flip-chip processors with a scalable layout and routing strategy
Q-chip
C-chip
Basic elements
Routing corridor between two qubit rows
Automation of design and simulation
Chalmers code
readout
Z
Z
XY
Z
XY
Z
XY
Z

## Slide 3: 1.1 General properties of quantum measurements
Desirable properties:
Projective and Quantum non-demolition (QND)
  Coupling to the meter does not change the state of the qubit
  Repeated measurement yields the same outcome.
Good ON/OFF ratio
𝐻𝑄𝑄, 𝐻𝑖𝑖𝑛𝑡
= 0.


𝐻𝑖𝑖𝑛𝑡 , 𝐻𝑚𝑒𝑡𝑒𝑟
𝐻𝑖𝑖𝑛𝑡 , 𝐻𝑚𝑒𝑡𝑒𝑟
= 0 during “OFF”
≠ 0 during “ON”
No spontaneous decay/excitation due to measurement apparatus
Fast and high fidelity
Controlled Coupling
𝐻𝑚𝑒𝑡𝑒𝑟
0 1
Qubit
“Meter”
=
Auxiliary system
𝐻𝑄𝑄
𝐻𝑖𝑖𝑛𝑡

## Slide 4: 1.2 Circuit QED
Light field confined
between mirrors
Input field
atom
Output
Light-matter coupling
System Hamiltonian (compare chapter 2):
S. Haroche & J. Raimond, Exploring the Quantum, OUP Oxford (2006)
LC
resonator
SC qubit
Circuit
equivalent
Resonator field qubit
coupling
Jaynes-Cummings Hamiltonian
Rotating wave approximation (RWA)
Two-level approximation
qubit decay
photon decay
2
1 𝐶𝑐
𝑔 ≈
𝐶𝑟𝑒𝑠𝐶𝑞
𝜔𝑔𝑔𝑒 𝜔𝑟

## Slide 5: 1.3 Circuit QED: Resonant case and dispersive limit
|
Christopher Eichler, HS 2019, QSSC |
Strong coupling regime:
quantized field
qubit
coupling
Jaynes-Cummings Hamiltonian:
What happens
in the limit of large detuning?
Dispersive coupling
01.11.2019 72
Limit of large detuning is referred to as the dispersive limit. No resonant exchange of excitations.
In the dispersive regime coupling Hamiltonian commutes with qubit Hamiltonian.
A. Wallraff et al., Nature 431, 162 (2004), J. Fink et al., Nature (London) 454, 315 (2008)
Energy level diagram for resonant case 𝜔𝑟 = 𝜔𝑔𝑔𝑒:
2𝑔

## Slide 6: 1.4 Principle of Dispersive Qubit Measurement
A. Wallraff et al., Phys. Rev. Lett. 95, 060501 (2005).
R. Vijay et al., Phys. Rev. Lett. 106, 110502 (2011).
In the limit of large detuning
:
2𝜒𝜒
Amplitude of
transmitted signal:
readout frequency
probe
field
I
Q
ADC
𝐴 𝑒
𝑖𝑖𝜙𝜙
= 𝐼 + 𝑖𝑖 𝑄𝑄
signal
amplitude
Phase
In-phase and quadrature components
output
field
,with 𝜒𝜒 ≈ −𝛼
𝑔𝑔2
Δ(Δ−𝛼𝛼)

## Slide 7: 1.5 Readout Resonator Response
Transmission amplitude or readout resonator extracted through Purcell filter for qubit prepared in ground (g) or excited (e) state :
Parameter fit (input-output model): Readout resonator r/2 = 37.5 MHz
State dependent resonator shift 2/2 ⋍ -16 MHz
In ground/excited state:
Data measured after state prep. (*,*) Fit to resonator response model (-)
Walter et al., Phys. Rev. Applied 7, 054020 (2017)

## Slide 8: 2.1 Control and Characterization of superconducting qubits
15um
XY control
Frequency
(Z) control
Current 𝐼(𝑡)
Φ(t)
Qubit island
On-chip control
Microwave drive 𝑏𝑖𝑖𝑛 t resonant with qubit frequency rotates Bloch vector about X and Y
+
𝑖𝑖𝑛 𝑖𝑖𝑛 𝑖𝑖𝑛
axis. Drive power 𝑃 = ℏ𝜔𝑏 𝑏 .
Arbitrary waveform generators (AWG) used to generate pulses, up-converted to the MW frequency band by mixing with a local oscillator field.
𝐶2𝑍𝑍 𝜔2
𝑐 0
𝐶Σ
Coupling rate to charge line 𝛾𝛾 = imposes
decay and therefore needs to be 𝛾𝛾 ≪ 1/𝑇1.
Tunability of the qubit achieved by sending a current 𝐼 𝑡 to a separate control line generating a magnetic flux Φ 𝑡 in the SQUID loop.
Used for both static (DC) control of the qubit frequency and for applying pulses on nanosecond timescales.
𝑖𝑖𝑛
Drive 𝑏 (t) at carrier
frequency 𝜔𝑔𝑔𝑒
Capacitance 𝐶
𝑐
mediates coupling with
rate 𝛾𝛾
Charge
line
Flux line

## Slide 9: 2.1 Control and Characterization of superconducting qubits

## Slide 10: 2.2 Measurement of Rabi oscillations
Qubit frequency 𝜔𝑔𝑔𝑒/2𝜋 = 5.758 GHz
determined spectroscopically.
Initialize qubit in ground state.
Apply pulse at 𝜔𝑔𝑔𝑒 with variable
amplitude Ω0.
Gaussian pulse envelop with characteristic 𝜎 ~ 5 − 10𝑛𝑠.
Readout qubit state and average over
~103 repetitions.
Sinusoidal fit to extract 𝜋- and 𝜋/2- pulse amplitude.
Ω0/Ω0,max
Excited state population 𝑝𝑒
𝜋 − pulse.
𝜋/2 − pulse.
Ω0

## Slide 11: 2.3 Measurement of dephasing time
Ithier, G. et al. PRB 72, 134519 (2005).
2
Initial 𝜋 -pulse prepares 𝑔 + |𝑒〉.
Map remaining coherence after time 𝑟 to excited
2
state using a second 𝜋- pulse, and measure.
Detune pulse by fIF = 0.5 MHz from qubit frequency to obtain oscillating pattern. → Higher accuracy in estimating the qubit frequency.
2
Fit Characteristic decay time 𝑇∗ = 13 𝜇s
In this case, decay reasonably well described by
exponential function 𝑒
−𝑐/𝑇
2
∗
Depending on spectral properties of the dominant noise source, decay better described by different functional form, e.g. Gaussian decay for 1/f – noise.
If relaxation is only source of decoherence: 𝑇2 = 2 𝑇1 (“T1 limit of dephasing time”).
𝑟 [𝜇𝑠]
readout
Excited state population 𝑝𝑒

## Slide 12: 2.3 Measurement of dephasing time
Low frequency noise can be partly compensated for by applying an echo 𝜋-pulse after 𝑟/2 to reverse the direction of the Lamor precision.
2
The resulting decay time 𝑇𝑒𝑐ℎ𝑜 = 18 𝜇𝑠 is longer
2
than 𝑇∗.
Explanation: Low frequency noise which causes the qubit frequency to change on timescales longer than 𝑟𝑚𝑎𝑥 will cancel out.
Variants of such dynamical decoupling sequences can be used to do noise spectroscopy → See e.g. Bylander et al., Nat. Phys. (2011)
𝑟 [𝜇𝑠]
Ithier, G. et al. PRB 72, 134519 (2005).
Excited state population 𝑝𝑒
Additional echo pulse
-

## Slide 13: 3.1 Characterization & Benchmarking of Quantum Processes
Ideally
|𝜓𝜓in〉
|𝜓𝜓out〉
𝑈
Realistically
𝜌in
𝜌out
ℰ
Questions:
General properties of the map ℰ?
How to measure the map ℰ?
  State and process tomography
Measure of distance between quantum states and processes: Fidelity
How to benchmark quantum gates with fidelities close to one?
  Randomized Benchmarking

## Slide 14: 3.2 Randomized benchmarking
Knill et al., PRA 77, 012307 2008
For simplicity, consider single-qubit case.
Apply sequence of 𝑛 gate operations 𝑈𝑖𝑖 before measuring.
Gates 𝑈𝑖𝑖 are chosen randomly from the Clifford group, mapping an element of the Pauli group to an element of the Pauli group. For a single qubit there are 24 Clifford gates.
Last gate 𝑈𝑛+1is chosen such that in the absence of errors state is brought back to initial state, i.e. 𝑈𝑛+1 … 𝑈2𝑈1 = 𝐼.
Average over 𝑚 different such sequences.
Success probability 𝑝0 to recover the initial state decays exponentially with # of gates 𝑝0 𝖺
𝛼𝑛, with depolarization parameter 𝛼.
𝑅𝐵
The error per gate is given by 𝜖𝜖 = 1 − 𝛼
space (d=2 for a single qubit).
(𝑑−1)
𝑑
where 𝑑 is the dimension of Hilbert
|0〉
0 1
𝑈
1
𝑈
2
𝑈
3
𝑈𝑛+1
…

## Slide 15: 3.3 Randomized benchmarking: Example single qubit gates
*Motzoi et al., PRL 103, 110501 (2009)
Pulse duration typically between 15 to 50 ns. Leakage into second excited state avoided by using (DRAG*) pulse parametrization.
Use Clifford decomposition in terms of X rotations and virtual Z gates (see McKay et al., PRA (2017)).
Population of ground state decays exponentially.
Fitted depolarization parameter 𝛼 ≈99.6% and gate error 𝜖𝜖 ≈ 0.2% in this example.
Orange dashed line indicates the limit expected when only considering qubit decoherence.
Deviation from coherence limit hints at finite control errors, e.g. resulting in leakage to the f- level.

## Slide 16: 3.4 Interleaved Randomized benchmarking (IRB)
Magesan et al., PRL 109, 080505 (2012)
Question how to characterize the fidelity of one particular Clifford gate 𝑉?
Compare decay of standard RB sequence …
…with result of a 2nd experiment, in which gate 𝑉 gets interleaved with random Clifford gates.
Difference between the depolarization parameters 𝛼𝑅𝐵 and 𝛼𝐼𝑅𝐵 results in an estimate for the
𝑉
error 𝜖𝜖 =
𝑑
𝑑+1
𝛼𝑅𝐵
(1 − 𝛼𝐼𝑅𝐵) per gate 𝑉.
Randomized Benchmarking can be generalized to multi-qubit gates.
|0〉 𝑈1 𝑈2 𝑈
0 1
3
𝑈𝑛+1
…
|0〉 𝑈
1
𝑈
2
𝑈
3
𝑈𝑛+1
…
𝑉
𝑉
𝑉
0 1